## Slide 1: Lab 1 Mininet/ONOS Installation

## Slide 2: Outline
Mininet
OpenDaylight
Add flow via REST API
Appendix
Reference

## Slide 3: Mininet
Download virtual disk from https://github.com/mininet/mininet/wiki/Mininet-VM-Images

## Slide 4: Mininet
Boot Mininet by Virtualbox, Vmware, Parallels Desktop

## Slide 5: Virtualbox
Mininet image
Ubuntu
Internal Network
NAT
Internet
Interface 1
Interface 2

## Slide 6: Virtualbox
Controller
Internal Network
NAT
Internet

## Slide 7: VirtualBox
Setup interfaces in Ubuntu
  sudo dhclient enp0s3
  sudo ifconfig enp0s8 192.168.100.1

## Slide 8: VirtualBox
Setup interfaces in Mininet
  sudo ifconfig eth0 192.168.100.2

## Slide 9: Virtualbox
double-click on the .ovf file and import it
If you get errors importing the .ovf file, you can simply create a new VM of the appropriate type (e.g. Linux, Ubuntu 64-bit) and use the .vmdk file as the virtual hard disk for the new VM.
Select “settings,” and add an additional host-only network adapter that you can use log in to the VM image. Start the VM.

## Slide 10: Vmware
Import the OVF file, then start the VM
VMware may ask you to install VMware tools on the VM - if it asks, decline

## Slide 11: Parallels Desktop
Use Parallels Transporter to convert the .vmdk file to an .hdd image that Parallels can use, and then create a new VM using that .hdd image as its virtual drive. Start the VM.

## Slide 12: Log in to VM
Account : mininet
Password : mininet

## Slide 13: Log in via SSH
VMware : ssh -Y mininet@[mininet’s ip address]
Virtualbox : Users who have set up a host-only network on eth1 should use sudo dhclient eth1 and check it has an ip address
  ssh -Y mininet@[mininet’s eth1 ip address]

## Slide 14: ONOS
Download ONOS package in the following website:
    https://onosproject.org/software/

## Slide 15: ONOS
Use cd command to ONOS folder
"./bin/onos-service start” to launch ONOS

## Slide 16: Activate OpenFlow
Use "feature install [feature name]" to install feature
To activate OpenFlow
    onos> app activate org.onosproject.openflow
Use feature:list -i to list all installed features
Check the following web site for more details:
    http://www.stackguy.com/archives/248
onos> app activate org.onosproject.openflow
onos> app activate org.onosproject.openflow

## Slide 17: launch mininet
sudo mn --mac --switch ovsk,protocols=OpenFlow13 —controller=remote,ip=[controller’s ip] --topo linear,2
sudo mn --mac --switch ovsk,protocols=OpenFlow13
--controller=remote,ip=192.168.100.1
--custom ./mininet/custom/test.py --topo mytopo
The file to setup a topology
The default topo with two switches

## Slide 18: test.py

## Slide 19: Topology

## Slide 20: Topology via Web Page
http://localhost:8181/onos/ui/index.html
Login/password = onos/rocks

## Slide 21: Mininet test
In mininet environment we can use h1 ifconfig to check what h1’s ip address it is.

## Slide 22: Install flow to vSwitch
We can use Rest API to install flow from controller to vswitch
curl -X POST -H "content-type:application/json" http://localhost:8181/onos/v1/flows/of:0000000000000001 -d @./test_1.json --user onos:rocks
Switch ID
Json file for the rule

## Slide 23: Install flow to vSwitch
The packet we want to match
Action (how to process the packet)

## Slide 24: Check Flow
ONOS web site
The flow which we add

## Slide 25: Test Traffic
Use iperf or ping
h1 ping h2
iperf

## Slide 26: Check Flow
Use sh ovs-ofctl dump-flows -O OpenFlow13 s1
The number of packets matching the rules

## Slide 27: Homework
h1 ping h2
產生有兩條路徑的topology
讓ping packet走較長的路徑
在NTU COOL上傳三張螢幕截圖:
  Switch s3的forwarding table
  Ping 成功的畫面
  ONOS GUI中的topology
Due: 4/1, 2024

## Slide 28: Topology

## Slide 29: reference
ONOS and mininet
  http://www.stackguy.com/archives/248
json for rule
  https://wiki.onosproject.org/display/ONOS/Flow+Rules
curl to install rules
  https://wiki.onosproject.org/display/ONOS/REST